## Slide 1: Final Project - Simple Microprocessor -
Logic Design Lab.
Spring 2018
Prof. Chang-Gun Lee
(cglee@snu.ac.kr)
TA. WonJae Jang
TA. Wonseok Lee
TA. Alena Kazakova
TA. Dongwan Kang
(ta@rubis.snu.ac.kr)

## Slide 2: Contents
Project Overview
Microprocessor Design
  Data Path
  Instruction Set Architecture
    Formats of the entire instruction set
    Control Signal Table
  Interface of Microprocessor components
  Example test set : Input/Output
  Test Environment
Project Grading

## Slide 3
RUBIS
3
Project Overview
Implement a Simple Microprocessor in Verilog and program it on FPGA. Mimic a real computer.
Your FPGA implementation should consist of an ALU, a control unit, a system memory, registers, and so on.
Use the on-board 50MHz clock oscillator to create 1Hz clock (1 tick per second).

## Slide 4
RUBIS
4
Project Overview
8-bit Microprocessor
Instruction size : 8-bit
# of instructions : 4 (add, load, store, jump)
Register size : 8-bit
# of registers : 4
Input : Instruction codes from external memory (TA’s FPGA)
  TA will test the result with the memory implemented in another FPGA chip. Several sets of instruction codes will be tested. Specific pin assignments between your microprocessor and instruction memory will be given.
Output : Current value of Reg Write Data.
  Use 7 segment displays. Display the value in Hexadecimal.
※ David A. Patterson, John L. Hennessy. (2005). Computer Organization and Design (3rd ed.). Morgan Kaufmann.

## Slide 5: Microprocessor Design – Data Path
Read Address
Instruction Memory
Instruction [7:0]
PC
Reg Write Data
Registers
Write Register
Read Register2
Read Register1
Read data1
Read data2
Address
Data Memory
Write Data
Read Data
ALU
Add
Add
MUX
MUX
Control
Instruction [7:6]
Instruction [1:0]
Instruction [3:2]
Instruction [5:4]
ALUOp
Branch
ALUSrc
External Memory
Output
1
Sign
extend
MemRead
MemWrite
RegWrite
MUX
MUX
MemtoReg
0
1
0
1
0
1
0
1
RegDst

## Slide 6: Microprocessor Design - Instruction Set Architecture
Formats of the entire instruction set
(8bit processor) |  |  |  |  |  |  |  |  |  |  |  | 
* op |  | operation code |  |  |  |  |  |  |  | * Registers (8bits) |  | 
rd |  | destination register |  |  |  |  |  |  |  | Program Counter(PC) |  | 
rs |  | source register |  |  |  |  |  |  |  | $s0 - $s3 |  | 
rt |  | source register two |  |  |  |  |  |  |  |  |  | 
imm |  | immediate (constant) |  |  |  |  |  |  |  | * Memories (8bits) |  | 
 |  |  |  |  |  |  |  |  |  | Instruction Mem. | address range: 0x00-0xFF | 
op, rd, rs, rt |  | unsigned value |  |  |  |  |  |  |  | Data Mem. | address range: 0x00-0xFF | 
imm |  | signed value |  |  |  |  |  |  |  |  |  | 
Machine Code |  |  |  |  |  |  |  |  |  |  |  | 
CMD | Type | Example |  |  |  |  |  |  |  | Meaning (Assembly Code) | Meaning (in C language) | Description
 |  | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0 |  |  | 
 | R | op |  | rs |  | rt |  | rd |  |  |  | 
 | I | op |  | rs |  | rt |  | imm |  |  |  | 
 | J | op |  |  |  |  |  | imm |  |  |  | 
add | R | 0 |  | 1 |  | 2 |  | 0 |  | add $s0, $s1, $s2 | $s0 = $s1 + $s2 | 3 operands, add with registers
lw | I | 1 |  | 3 |  | 0 |  | 0 |  | lw $s0, 0[$s3] | $s0 = Mem[$s3+0] | transfer value from memory to reg.
sw | I | 2 |  | 3 |  | 0 |  | 1 |  | sw $s0, 1[$s3] | Mem[$s3+1] = $s0 | transfer value from reg. to mem.
j | J | 3 |  |  |  |  |  | -2 |  | j -2 | go to (next PC -2) | jump to next PC with an offset
※ for Add operation, you don't have to care about the overflow.
※ only the immediate is signed value, other values are unsigned

## Slide 7: Microprocessor Design - Instruction Set Architecture
Control Signal Table
Signal Name | Effect when deasserted (0) |  |  |  | Effect when asserted (1) |  |  | 
RegDst | The register file destination number for the Write register comes from the rt field (bits4-5) |  |  |  | The register file destination number for the Write register comes from the rd field (bits2-3) |  |  | 
RegWrite | None |  |  |  | Write result to rd |  |  | 
ALUSrc | The second ALU operand comes from the second register file output (Read data 2) |  |  |  | The second ALU operand is the sign-extended, lower 2 bits of the instruction |  |  | 
Branch | The PC is repaced by the output of the adder that computes the value of PC + 1 |  |  |  | The PC is repaced by the output of the adder that computes the branch target |  |  | 
MemRead | None |  |  |  | Data memory contents designated by the address input are put on the Read data output |  |  | 
MemWrite | None |  |  |  | Data memory contents designated by the address input are replaced by the value on the Write data input |  |  | 
MemtoReg | The value fed to the register Write data input comes from the ALU |  |  |  | The value fed to the register Write data input comes from the data memory |  |  | 
ALUOp | None |  |  |  | Choose ALU operation (in this project, only Add operation exists. So this signal is not effective, but is for later expandability) |  |  | 
Instruction | RegDst | RegWrite | ALUSrc | Branch | MemRead | MemWrite | MemtoReg | ALUOP
R-format | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 1
lw | 0 | 1 | 1 | 0 | 1 | 0 | 1 | 0
sw | x | 0 | 1 | 0 | 0 | 1 | x | 0
j | x | 0 | 0 | 1 | 0 | 0 | x | 0
David A. Patterson, John L. Hennessy. (2005). Computer Organization and Design (3rd ed., pp.306). Morgan Kaufmann. |  |  |  |  |  |  |  | 

## Slide 8: Microprocessor Design – Interface of Microprocessor components
Program Counter
  Indicates the address of instructions. Initially, PC is set to start address as zero.
Register
  Consists of four 8-bit general purpose Registers.
  Write data to Register or output the read data from Register according to control inputs.

## Slide 9: Microprocessor Design – Interface of Microprocessor components
Instruction Memory
  Instruction size : 8-bit
  # of instructions : 4 (add, load, store, jump)
  It has pre-defined instructions. Each instruction is 8-bit long. 2 MSBs are the instruction, remaining LSBs are used for different purpose. (Refer to ISA format)
  # of input ports : 8 (8-bit Instruction Address)
  # of output ports : 8 (8-bit Instruction Register)
  Assume Instruction Memory for test. Instruction Memory will be given by external memory on evaluation by TA.
Instruction [7:0]
Address [7:0]

## Slide 10: Microprocessor Design – Interface of Microprocessor components
Control Unit
  Manages the process of moving data and instruction.
  Get 2-bit operation as input and outputs 1-bit control signals (Refer to Control Signal Table)
ALU
  Performs add operation (don’t care ‘overflow’)
  Two operands (such as Rs, Rt, offset of I-type instructions)

## Slide 11: Microprocessor Design – Interface of Microprocessor components
Data Memory
    8-bit address, # of data : 256 But, because of the total capacity of the FPGA we use, we will use only 32 of 8-bit registers
    Initialize the data memory like above. This means, when you press 'Reset' button, data should be like above. (hint: use always block sensitive to reset signal.)
Data Memory
[0] 0
[1] 1
[2] 2
[3] 3
...
[14] 14
[15] 15
[16] 0
[17] -1
[18] -2
[19] -3
...
[30] -14
[31] -15

## Slide 12: Microprocessor Design – Interface of Microprocessor components
Output 7 segment display
  Two 7 segment displays that show the contents of Register for Reg Write Data in Hexadecimal.

## Slide 13: Microprocessor Design – Interface of Microprocessor components
Read Address
Instruction Memory
Instruction
FPGA
FPGA
Instruction
50MHz Oscillator
RST
LED1
LED2
PC
Microprocessor

## Slide 14: Example test set : Input
[1] lw $s1, 0($s0) // 2’b01 2’b00 2’b01 2’b00
[2] lw $s2, 1($s0) // 2’b01 2’b00 2’b10 2’b01
[3] add $s0, $s1, $s2 // 2’b00 2’b01 2’b10 2’b00
[4] sw $s2, 1($s0) // 2’b10 2’b00 2’b10 2’b01
[5] j -1 // 2’b11 2’b00 2’b00 2’b11
signed value in
2’s complement.
Refer to ISA
The actual machine instructions
stored in Instruction Memory
[0] 0
[1] 1
[2] 2
[3] 3
Data Memory
Data stored in
Data Memory
…
Instructions

## Slide 15: Example test set : Output
Result
  Reg Write data in Register becomes 2 (ALU result. But don’t care)
  PC is fixed as 4 (infinite loop)
  Data Memory’s memory [2] becomes 1
[0] 0
[1] 1
[2] 1
[3] 3
Data Memory
…
4
PC
Reg Write data : 1
[0] 1
[1] 0
[2] 1
[3] 0
Register

## Slide 16: Test Environment

## Slide 17: Test Environment
Instruction[7:0]
Read_Address[7:0]
Reg_Write_Data
[7:4]
Reg_Write_Data
[3:0]

## Slide 18: Test Environment
Cable will be available in material cabinet after June 7th
(Or you can make your own)

## Slide 19: Project Grading
Report (individual) (40%)
  Explain the overall design and structure in detail
  Specify the functionality of each module in your implementation
  Verify your implementation is correct with simulation result
Completeness (60%)
  Sets of Test Instructions (testing from basic operations to combinations of operations) will be tested
Extra credits (5%)
  Basic functions + “alpha”
  Extra implementation that we can see when grading your project score. Any useful extra implementations, such as Register status displays or operation displays etc., are okay

## Slide 20: Project Grading
Date : June 19th, Tue
Time : 15:30
Location : B302 R310-2
Report & Code Submission : until 19th, June. 15:30 via e-mail
FPGA Submission : right after the test. If the FPGAs are broken or missing, you will get the 20% penalty of your final project.

## Slide 21: Calendar
Final
Exam
Project
Due
Today

## Slide 22: End
한 학기 동안 고생 많으셨습니다